## Slide 1: Arduino Workshop #3
Using Transistors and Driving Motors and Servos
Notes: 24 – Arduino Uno
24 – USB cable
24 – 9 V battery clip
24 – 9 V battery
24 – 5V L4940V5 Linear regulator
24 – 22 µF electrolytic capacitor
24 – 0.1 µF electrolytic capacitor
24 – 1 µF ceramic capacitor
96 – Blue LED
96 – 1 kΩ resistor
24 – PN2222 NPN BJT transistor
24 – jumper wire set
24 – Sharp GP2Y0A41SK0F IR distance sensor (with cable)
24 – Standard servo motor
24 – DC motor
24 – Breadboard
24 – Potentiometer
24 – SN754410 H-Bridge IC
24 – 1N4004 Diode

## Slide 2: PowerPoint and Code
Github.com/EELabMan
Go To Repositories and find Arduino 3 Motors and Servos

## Slide 3: Warning
In this lesson you will be using a 9 volt battery to power motors. This voltage is not physically dangerous, but if hooked up improperly could damage the electronics in the circuit. When wiring your circuits you should avoid short circuiting (connecting power directly to ground) and you should not hook up two separate voltage sources to each other (DO NOT hook the 9 v and Arduino 5 v to the same power row on the bread board)

## Slide 4: What is a “DC Motor”?
DC motors
  Found in devices around your house
  Rotate continuously when a dc voltage is applied to them
  Come in an array of sizes
  Very cheap to produce
  Rotation is dictated by the voltage applied to them
    Lower voltage -- slower speed
    Reverse voltage -- reverse direction of rotation
  Two main types
    brushed
      Employ stationary magnets and spinning coil
      Electricity is transferred to the coil via “brushes”
      Cheaper
      Wear out more easily
    Brushless
      Work using inductive forces to rotate
      Can generate electricity if manually rotate the rotor
      Example stepper motors

## Slide 5: Handling High current inductive loads
DC motors generally require more current than an Arduino can provide
Can create harmful voltage spikes
  We need to isolate them from our Arduino
  Transistor allows the safe switching of motors state
  We can control the speed using PWM (as learned earlier)

## Slide 6: Schematic
Before we hook up a motor let's take some time to look at each component
Q1 - NPN transistor
    A “voltage controlled switch”
R1 - 1 ㏀ resistor
  separates the transistor from the Arduino
M1 - The DC motor
C1 - 1 µF capacitor
  filter noise
D1 - diode
  Protects the power supply from reverse voltage caused by the induction of the motor

## Slide 7: Using transistors as a switch
A transistor is a device that regulates current or voltage flow and acts as a switch or gate for electronic signals
We are using Bipolar junction transistors (BJT)
Each BJT has 3 pins
  Emitter
  Collector
  base
Current flows through the collector and out the emitter
  By modulating base pin voltage you can control when current is allowed to flow
  5 v is more than adequate to open a transistor

## Slide 8: Labeled transistor Pic

## Slide 9: Protection Diodes
It is important to consider issues caused by DC motors
DC Motors act as inductors
  Electrical devices that store energy in a magnetic field and resist changes in current
As they spin they build up energy as inductance in the magnetic coils
When the power is removed this energy is released
  Inverted voltage spike
This is where we need a diode
  Diodes only allow current to flow in one direction
  By placing it in parallel with the motor the reverse voltage cannot exceed the forward voltage

## Slide 10: Now we know why each part is there, lets wire a circuit
Adding tape as a “flag” to the rotating shaft will let you visually see the rotation

## Slide 11: And the code to make it run
Download motor.ino from the github page and upload it to the Arduino

## Slide 12: Let's add to it
By combining our new knowledge of DC motors and our previous knowledge of analog sensors
  We can add a potentiometer to manually adjust the motor speed

## Slide 13: Wire it up

## Slide 14: Change the code a bit
Download motor_pot.ino from the github page and upload it to the Arduino

## Slide 15: Using an h bridge to control direction
Until now we have been spinning in one direction
What if we want to change the direction of spin?
  The H- Bridge accomplishes this

## Slide 16: Whats an H-Bridge?
By closing any 2 switches the motor responds differently
  Close S1 & S4
    Motor spins one direction
  Close S2 & S3
    Motor spins the opposite direction
  Close S1 & S2
    SHORT CIRCUIT!
  Close S3 & S4
    SHORT CIRCUIT!

## Slide 17: Warning
Be aware of the main issues that plague an H-Bridge.
A direct short to the power source (closing S1 & S2).
Because we are using a 9 V battery, a shorted battery heats up and could cause a leak or fire
To ensure you don't blow anything up, always disable the chip before switching the state of any switches

## Slide 18: H-bridge Pinout and function table
Integrated circuits (ICs) are numbered from top left counter clockwise
  There is always an indication of top of the chip
    Notice the “half circle”

## Slide 19: How to understand the H-Bridge
Which pins we are using
  GND (pins 4,5,12,13)
    These pins connect to a shared ground
  Vcc2 (pin 8)
    Supplies motor current (connect to 9 V)
  Vcc1 (pin 16)
    Supplies chip logic power (connect to 5 V)
  1Y & 2Y (pins 3 & 6)\
    Output for the left driver (connect to motor)
  1A &2A (pins 1 & 7)
    State definition pins (connect to Arduino to toggle state)
  1,2En (pin 1)
    Enables or disable left driver (connect to Arduino to control speed dynamically)
  3Y &4Y (pin 11 & 14)
    Right driver pins (not being used in this project)
  3A & 4A
    State switches for right driver (not in use this project)
  3,4EN
    Enables or disable left driver (connect GND for this application)

## Slide 20: Lets wire it up

## Slide 21: Download and run hbridge.ino
Note for each function:
EN is always set low then the MC1 And MC2 is adjusted
By using PWM we can change the duty cycle
rate must be between 0 and 255 (this happens in the main loop)

## Slide 22: Driving servos

## Slide 23: Servos
DC motors are fine if you don't need feedback
  You never know exactly where they are in their rotation
Servos solve this by rotating to a specific angle
  And then staying at that angle until controlled to a new rotation angle

## Slide 24: How servos work
Servos work in two ways
  Unmodified
    Rotation limited to between 0 and 1800
      A potentiometer in line with the servo reads a pulse width length and converts that to angle of rotation
      The length of the pulse needed is between 1 ms and 2 ms
        1 ms 5 v pulse - turns servo to 00
        2 ms 5 V pulse - turns servo to 1800
        1.5 ms 5 V pulse - turns servo to 900
        To remain in position (if under load) you can resend the same width pulse every 20 ms
  modified
    Rotation is uninhibited
      With no potentiometer inline, the pulse length dictates servo speed (and it can rotate 3600 as needed)
Three pins
  Power (usually red)
  Ground (usually black)
  Signal (usually white or orange)
They can be ran on 5 V but building a separate power supply is common

## Slide 25: A diagram to clarify

## Slide 26: Servos can run on 5 V but need more current
We will employ a linear regulator
Simple device
Has three pins
  Input voltage
    Must be higher of the voltages used
  Output voltage
    Lower voltage (set by the regulator being used)
  Ground
The drop in voltage results in heat
output is maintained even as the input voltage changes over time (think battery slowly draining)

## Slide 27: Linear regulator schematic
Notice the capacitors
  These are decoupling capacitors
The 5 V rail created needs to be separate from 5 V on the arduino
Ground should be grounded w/ arduino

## Slide 28: Lets wire up a servo (and regulator)
Notice the regulators orientation
Metal tab is in the “back”
Battery on the left most pin
Ground on center pin
Servo power on the rightmost pin
Pins shouldn't touch (shorts are bad)
The stripe indicates negative terminal and should be connected to a common ground

## Slide 29: Download and run servo.ino
The Arduino library makes controlling servos easy
The statements
Include
  Adds functionality of libraries (in this case Servo)
Servo myServo
  Makes a servo object named “myServo”
  If you have multiples you can call them all different names

## Slide 30: Building a distance sensor
If time permits

## Slide 31: Use the knowledge gained from the past
To build this we will use
  IR distance mounted to a servo
  4 LEDS
    To correspond to four quadrants of the sweep
Why IR?
  Infrared light (IR) is part of the electromagnetic spectrum that is invisible to humans but can be “seen” by IR sensors

## Slide 32: Lets build it
Start by attaching the IR receiver to a servo
  Hot glue or putty or tape can be used
Hook up servo to Arduino 5 V regulator to power it
The IR receiver replaces the potentiometer and plugs into pin 0
Four LEDS plug into pins 3,5,6 & 11
  With a 1 ㏀ resistor
YOU CANT USE pins 9 & 10 when using the servo library

## Slide 33: Diagram to follow

## Slide 34: The code should
Rotate to a given position
Measure distance
Convert it to a value that can be used for the led
Change the LED'S brightness
Move to the next position
Repeat
Give it a try yourself (we will look at one solution near the end)

## Slide 35: Download and run sweep.ino
Code section 1
Code section 2

## Slide 36: Stay tuned
Arduino 4 will cover Serial Communications.
We’ll send temperature sensor data to the computer and display it using Java!